## Slide 1: Building an open source potentiostat

## Slide 2: The research objective
Anoxic bottom water layer at Nomilu Fishpond (Kaua’i)
Characterize redox-geochemical cycles
  Oxidation partners for oxidation of organic matter
    NO3, Mn
  Anoxygenic photosynthesis?

## Slide 3: Voltammetry
Measuring the current generated by reduction/oxidation of analyte at electrode surface
  Analytes: Fe(II), Mn(II), H2S, O2 etc
Reaction potential is specific to analyte, peak height relative to concentration
Electrode: Mercury/Gold
Potentiostat: Applies potential to electrode, measures current
http://article.sapub.org/10.5923.j.ajee.20140406.07.html

## Slide 4: Dstat – open source potentiostat
Dstat
  Open source hardware design
  Open source (python) software
  Cost: ~130 $US for parts
  Size: 80x80 mm
  Assembly required
Commercially available Potentiostat
  Black box
  Proprietary software
  Cost: thousands
  Big box
  Comes assembled
Potential Issues:
Sensitivity
Noise
To our knowledge, the Dstat design has successfully been tested with nA current measurements but not with Hg/Au electrodes